extent = contiguous area of storage in a computer file system, reserved for a file.
- When a process creates a file, file-system management software allocates a whole extent
- When writing to the file again, possibly after doing other write operations, the data continues where the previous write left off
- This reduces or eliminates file fragmentation and possibly file scattering too.

cache write policy (write on disk)
1. Write-through - Write is done synchronously both to the cache and to the backing store
2. Write-back (or Write-behind) - Initially, writing is done only to the cache. The write to the backing store is postponed until the cache blocks containing the data are about to be modified/replaced by new content.

Many drives use a write-back cache in order to speed up the performance of writes.
With a RAID controller with battery-backed controller cache and cache in write-back mode, you should turn off barriers

Production:

mount option
type xfs (rw,noatime,nodiratime,nobarrier,logbufs=8,logbsize=256k,noquota)

barrier - Barrier support will flush the write-back cache at the appropriate times
Using write barriers with hardware write-back cache is not recommended and will in fact lower performance. Therefore, it is recommended to turn off the barrier support and mount the filesystem with "nobarrier".

logbuf - tell xfs how many blocks of 32K of journal information to keep in RAM. Default (and minimum) is 2, and maximum is 8.

logbsize - number of log buffers

xfs options

meta-data=/dev/sdy isize=256 agcount=5, agsize=268435424 blks
        = sectsz=512 attr=2
data = bsize=4096 blocks=1123220736, imaxpct=5
        = sunit=32 swidth=736 blks
naming =version 2 bsize=4096 ascii-ci=0
log =external bsize=4096 blocks=32768, version=2
        = sectsz=512 sunit=32 blks, lazy-count=1
realtime =none extsz=4096 blocks=0, rtextents=0

inode
The XFS inode contains
- fixed-size part
- variable-size; can contain: directory data, for small directories; attribute data, for small attribute sets; symbolic link data, for small symbolic links; the extent list for the file, for files with a small number of extents; and the root of a tree describing the location of extents for the file, for files with a large number of extents.

size - mininum (and default) value is 256 bytes, max is 2048
setting the inode size is important, as XFS stores xattr data in the inode. If the metadata is too large to fit in the inode, a new extent is created, which can cause quite a performance problem. Upping the inode size to 1024 bytes provides enough room to write the default metadata, plus a little headroom.

XFS can store small attributes directly in the inode if space is available in the inode. If the attribute fits into the inode, then it can be retrieved and modified without requiring extra I/O to retrieve separate attribute blocks. The performance differential between in-line and out-of-line attributes can easily be an order of magnitude slower for out-of-line attributes.

 For the default inode size of 256 bytes, roughly 100 bytes of attribute space is available depending on the number of data extent pointers also stored in the inode. The default inode size is really only useful for storing a small number of small attributes.

 Increasing the inode size at mkfs time can increase the amount of space available for storing attributes in-line. A 512 byte inode size increases the space available for attributes to roughly 350 bytes; a 2 KB inode has roughly 1900 bytes of space available.

 There is, however, a limit on the size of the individual attributes that can be stored in-line - there is a maximum size limit of 254 bytes for both the attribute name and the value (that is, an attribute with a name length of 254 bytes and a value length of 254 bytes will stay in-line). Exceeding these size limits forces the attributes out of line, even if there would have been enough space to store all the attributes in the inode.

agcount - XFS filesystems are internally partitioned into allocation groups, which are equally sized linear regions within the file system. Files and directories can span allocation groups. Each allocation group manages its own inodes and free space separately, providing scalability and parallelism — multiple threads and processes can perform I/O operations on the same filesystem simultaneously.

if you have a workload that has a heavy concurrent metadata modification workload, then increasing the number of AGs might be a good thing. I tend to use 2x the number of CPU cores as a general rule of thumb for such workloads but the best tunings are highly depended on the workload so you should start just by using the defaults. :)

Fragmentation = file is split and stored in non-contiguous extents. Fragmentation is a drag on performance, since reading a file now requires the read mechanism to jump from one extent to another to reassemble the whole file.

Masstest server:
actual 28924199, ideal 28821173, fragmentation factor 0.36%

root@safe193:~# time xfs_db -c frag -r /dev/sdn
actual 39906336, ideal 39830748, fragmentation factor 0.19%

safe209:~# time xfs_db -c frag -r /dev/cciss/c1d2p1
actual 28319835, ideal 28243782, fragmentation factor 0.27%

real 12m38.014s
user 0m18.569s
sys 1m23.493s

UNLINK

http://git.kernel.org/?p=linux/kernel/git/torvalds/linux-2.6.git;a=blob;f=Documentation/filesystems/xfs-delayed-logging-design.txt

Like many operations in XFS, deleting an entry from a
directory requires the creation of entries in the XFS
log. These entries record the net effect of the delete
operation, allowing the delete operation to be reconstructed
(more or less) in the event of a crash.

A transaction in the log records information about
critical data structures and how they will change as
the result of an operation. Log entries get saved to
disk in such a way that following a crash, the file
system can be put into a consistent state quickly by
"replaying" entries recently recorded to the log.

If you perform a number of operations on the same object
(such as removing multiple files from the same directory),
XFS currently sends copies of some of the affected data
structures to the log repeatedly--once for each operation
in sequence.

So for example if you delete lots of files from the same
directory, there is a consequently large volume of log
activity that needs to be performed, often describing
updates to the same data structure. Such a structure
will (currently) get written to disk many many times
as a result.

Dave recently added support for "delayed logging" to
XFS. It's currently an experimental feature, enabled
via a mount option. When delayed logging is active,
some log activity is held off, allowing numerous
updates to the same data structure to be aggregated.
A logged data structure can then be committed to disk
much less frequently, reducing the amount of data that
needs to be written to disk while preserving the ability
to recover the file system following a crash.

This optimization allows certain operations (like
mass deletions) to be completed much more efficiently,
and in the case of large directories the performance
improvement that results can be significant.

In any crash situation, there will be a certain amount
of file system activity underway at the time of the
crash that will be lost; logging file system operations
doesn't eliminate that possibility. The down side of
delayed logging is this type of loss is likely to be
greater than it would be with the more conventional
XFS logging mechanism. This is a tradeoff between
file system performance in normal operation and the
amount that can be recovered after a crash.

Ideal read performance for a given file is obtained when its data is stored in a contiguous manner because it avoids the penalty of seek operations. Translated in XFS terms, read performance is inversely proportional to the number of extents used.

 Extents are allocated transparently by XFS presumably in a way that minimizes fragmentation. As an example writing 100 files of 100MB each simultaneously to disk results in an average of 15 to 20 extents / file. If file size is dropped to 1MB fragmentation is reduced to 1 to 2 extents / file.

 Considering the numbers above, it is reasonable to assume that given XFS's allocation of disk space, fragmentation is not a problem for files below 1MB in size. In order to obtain visible improvements, we need to focus on larger files.