The Linux Programming Interface
Michael Kerrisk

1. Intro
Unix = OS developed in 1969, first in assembly and then in C
Linux = Unix-like operating system of which the Linux kernel forms a part
Linux distro = GNU packages + Linux Kernel + non-GNU packages

SUSv3 = Single Unix Specification

2. Fundamental concepts
shell = command interpreter = program which reads user's commands and executes them

file descriptor = non-negative integer; index on file descriptor table
file descriptor table = per-process table containing pointers to all open I/O streams

3. System programming concepts

system call = entry point into Kernel, allowing a process to request the kernel to perfom some action;	accessible via glibc wrappers

application calls wrapper
wrapper:
copies sycall arguments to CPU registers
copies the syscall number into CPU register %eax
executes a trap machine instruction (int 0x80) → CPU switches from user to Kernel	mode
Kernel invokes system_call routine

syscall has overhead because:
* the system must switch to kernel mode
* kernel must verify arguments
* kernel must transfer data between KVA and VAS

4. File I/O
if open() succeeds, it returns the smallest available file descriptor;
to open a file using fd 0:
close(STDIN_FILENO)
open file
or use dup2()

opening a file with O_APPEND guarantees that write operation happen atomically

check flags on a file descriptor:
flags = fcntl(fd, F_GETFL)
if (flags & O_SYNC) ….
set flag on a file descriptor:
flags |= O_NONBLOCK
remove flag on file descriptor:
flags &= ~O_NONBLOCK

scatter/gather I/O: readv(), writev()
* could be useful for writing headers
6. Processes
Text segment – executable code
Data segment (bss) (initialized + uninitialized): global vars
Heap: dynamic memory
Unused memory
Stack: contains stack frames

Stack grows downward, heap upward

Stack frame:
* function arguments and local variables
* call linkage information

7. Memory allocation
program break = current limit of heap; can be detected via sbrk(0)
brk(), sbrk() = change the location of the program break

in general, free() doesn't lower the program break; instead, is placing blocks of memory onto the free list

when malloc() allocates the block, it allocates an extra integer to hold the size of the block
free() reads this integer and knows which size the block is

page fault = a trap (interrupt) to the software raised by the hardware when a program accesses a page that is mapped in the virtual address space, but not loaded in physical memory. In the typical case the operating system tries to handle the page fault by making the required page accessible at a location in physical memory or terminates the program in the case of an illegal access.
- page faults are degrading the performance of a program

thrashing occurs when a computer's virtual memory subsystem is in a constant state of paging, rapidly exchanging data in memory for data on disk, to the exclusion of most application-level processing. This causes the performance of the computer to degrade or collapse.

9. Users

effective uid = uid associated to a process and who determines the permissions of the process
- if an executable file is owned by root and has set-user-ID bit enabled, the process will run with root privileges

10. Time
real time (wall clock) = elapsed time from start till end
process time = amount of CPU time used by a process
process time is separated into User and System time

specify a timezone when running a program: set TZ environment variable

localization = program automatically does the right thing when performing I/O (language, date format etc.); done via locale definitions (files in /usr/share/locale)
Part 2. Advanced features

13. File I/O Buffering

buffer cache = kernel-space buffer where/whence data is copied via write()/read()

Buffering of input and output data is done:
* by the kernel (flushing is done via sync())
* by stdio library (flushing is done via flush())

posix_fadvise() = syscall that informs the kernel about a likely pattern to access data

direct I/O = bypassing the buffer cache; use flag O_DIRECT when opening a file
* can considerably degrade performance, because kernel applies some optimizations (sequential read-ahead, I/O in clusters of blocks, sharing of buffers in cache etc.)

14. File systems

Each device is represented by:
* device driver
* device file

Device driver
kernel software layer that makes a hardware device respond to a well-defined programming interface (canonical set of VFS functions: open, write, read etc. that controls a device)

Device files
I/O devices are treated as files
block - access randomly
character - either cannot be accessed randomly (soundcard), either takes to long time
write on /dev/lp0 --> directly print

Block-device drivers
sector = group of adjacent bytes; basic unit of data transfer; never possible to transfer less than a sector
block = large number of adjacent bytes; power of 2, no larger than a page frame; multiple of sector size

Filesystem = organized collection of files and directories; consists of:
* superblock
* inode table
* data blocks
* dentries

Inode contains 15 pointers to the data blocks of file.

VFS = abstraction layer for file system operations

15. File attributes

sticky bit – for directories, acts as restricted deletion: unprivileged user can unlink files in a dir only if it has write permissions on dir and owns the files
* useful when having a directory which is shared between multiple users (commonly set on /tmp directory)

umask = file mode creation mask = specifies which permissions bits should always be turned off
default: 022 (----w--w-)

extended file attributes: i-node flags set on files or directories (chattr, lsattr)
* immutable, don't update last access time etc.

18. Directories

directory = file with a special organization; a table consisting of filenames and inodes

rm command:
* removes a filename from a directory list
* decrements the link count for corresponding inode
* if count == 0 ---> deallocates inode and data blocks to which it refers

if the string forming symlink's content is small enough, it will be stored in inode (saving the allocation of a disk block)

19. Monitoring file events

inotify = mechanism to monitor file events
* is not recursively monitoring

20. Signals

signal = a notification to a process that an event has occurred
Types of events:
* hardware exception (dividing by 0, referencing invalid memory etc.)
* user signals (interrupt, suspend etc.)
* software event (child has terminated, window resized, input available on a file descriptor etc.)

signal pending = state of signal between generated and delivered

standard signals: 1..31

SIGHUP – used for daemons to reload configuration, re-initialized themselves
SIGTERM – gracefully end
SIGKILL – can't be blocked, ignored or handled
SIGUSR1,2 – programmer-defined purposes

sigaction() is the preferred API for establishing a signal handler

- delivery of a signal is blocked while the handler is executing; if generated while the handler is executed, will be later delivered when handler returns
- signals are not queued (will be delivered only once)

Designing signal handlers

Write simple signal handlers!
* sets a global flag and exits; main program periodically checks this flag

reentrant function = function that can be safely simultaneously executed by multiple threads (e.g a function which employs only local variables)

When writing signal handlers:
* ensure that the code of signal handler is reentrant and that it calls only async-signal-safe functions (do not use functions which update internal data structures for buffered I/O: printf, scanf, cout etc.)

sigaction flags:
SA_SIGINFO – the signal handler will receive additional info about a signal
SA_RESTART – many system calls will be restarted (without the need for manually check EINTR etc.)

core dump = file containing a memory image of a process

The kernel could put a process to sleep:
* TASK_INTERRUPTIBLE
- waiting for some event
- process is woken up by the delivery of a signal
- processes are listed with state S

* TASK_UNINTERRUPTIBLE
- waiting on disk I/O
- signal is not delivered until the process emerges from this state
- listed with D

* TASK_KILLABLE
- wakes the process if a fatal signal is received

realtime signals (SIGUSR1, SIGUSR2) = POSIX addition to original signal mode
* are queued
* possible to specify data (an integer or pointer value) that accompanies the signal
* have a specified delivery order

sigsuspend() – wait for a signal

Part 3. Processes and programs topics

24. Process creation

fork() – creates a new process
* same text segment (which is read-only: a process cannot modify its code)
* separate copies (exact duplicates) of data, heap and stack segments (actually, copy-on-write)
* descriptors are duplicated (as if using dup())

good practice:
* child(ren) should use _exit(), parent should use exit()
* flush buffers before fork() (to avoid duplicated output)
* don't mix fork() and threads (child process is created with a single thread: the one that called fork(), but state of global variables like mutexes are preserved)

Control a process' memory footprint
problem: func() causes memory leaks and cannot be modified;
solution: call func() in a child and exit from it
fork():
//child
exit(func(arg))
//parent
wait(&status)

after fork(), the order of execution is not guaranteed
signals can be used to synchronize parent-child
child: kill(SIGUSR1)
parent: sigsuspend()

A process can terminate:
* normally: using _exit (which is called by exit() or when main() returns)
main() →
exit() →
_exit()
* abnormally: caused by the delivery of a signal

Monitoring child processes:
* using wait()/waitpid(), blocking and non-blocking(WNOHANG)
* establishing a handler for SIGCHLD

File descriptors and exec

$ ls -l > tmp.txt
- fork() is performed to create a child process
- child opens tmp.txt using file descriptor 1 (using dup2())
- child execs ls
- ls writes to stdout, which is the file tmp.txt

shell built-ins – commands executed by the shell, without fork() and exec()

- library functions should always set close-on-exec flag
- setuid and setgid programs should never use system() : shell's reliance on various environment variables opens a door for security breach

Interpreter scripts
interpreter = program which reads commands and executes them
#!interpreter-path [optional args]
when executing the script:
interpreter-path [optional args] script-path …

29. Threads

thread = lightweight process; sequence of instructions that may execute in parallel with others

each thread:
* has a private stack for local variables
* shares the same global and heap variables with other

Multithreaded:
+ sharing data is easy
+ creation is faster
- functions must be thread-safe
- a bug in one thread could damage all threads in a process
- all threads compete on the same VAS of host process → for large number of threads, memory exhaustion

good practice:
* avoid the use of signals in multi-threaded programs
* don't mix fork and threads

Thread lifecycle:
* pthread_create()
* pthread_exit() (if any thread calls exit(), all threads immediately terminate)
* pthread_detach() or pthread_join()

on Linux, mutexes are implemented using futexes = fast user-space mutex

good practice:
* define a mutex hierarchy: threads should always lock mutexes in the same order

thread-specific data = technique for making an existing function thread-safe, without changing its interface
* allows a function to maintain a separate copy of a variable for each thread that calls the function

Dealing with asynchronous signals:
* block the signals in the main thread before any other thread is created (all subsequent threads will block the signals)
* create a single dedicated thread that accepts incoming signals, using sigwait()

34. Process groups and sessions

process group = a set of one or more processes sharing the same process group identifier
setgpid()

session = a collection of related process groups
setsid(), getsid()
only one process can be in the foreground at a particular moment

35. Process priorities and scheduling

nice = niceness to other processes; the higher the value, the lower the priority

- wherever possible, a process is rescheduled on the same CPU (switching to another is expensive because process data has to be discarded from the cache of old CPU and loaded in the cache of new CPU)

cache line = size of the unit used for transfers between CPU cache and main memory

37. Daemons

daemon:
* long-lived process
* runs in background and has no controlling terminal

Creating a daemon:
1. fork(), parent exits and child continues
- the child process is guaranteed not to be a process group leader, therefore is able to do #2
(process group leader is prevented to execute setsid() because it would be able to place itself in another new session, while other members of the process group remained in the original session)

2. setsid(): starts a new session and free itself from any association with a controlling terminal

3. fork(), parent exits and the (grand)child continues
- ensures that child is not a session leader and can never reacquire a controlling terminal

4. clear the process umask, to ensure that newly-created files and directories have the requested permissions

5. change cwd to /
- if cwd of daemon is on a file system other than the one containing /, it cannot be unmounted

6. close all fds inherited from the parent (0, 1 and 2)

7. open /dev/null to make descriptors 0, 1 and 2 refer to this device
- if a library function performs I/O on this descriptors, it won't unexpectedly fail

syslogd accepts log messages from:
- a UNIX domain socket, /dev/log (locally produced messages)
- UDP socket (messages sent across TCP/IP network)

syslog API:
- openlog() - establish default settings that apply to subsequent calls to syslog()
- syslog() - logs a message
- closelog() - close the connection to the log

Chapter 40. Login accounting

utmp, wtmp = data files containing information about users logging in and out of the system

Chapter 41. Shared libraries
library
Linker

Compiler

Code	object file	executable

object file = file containing object code; produced by a compiler
library = a set of object files grouped together; produced by a linker

Static library (archives): a set of object files
* used to build multiple executables without recompiling (executable includes copies of all object files)
* simplifies the link command
* created with ar
* linked against with -l

disadvantages:
* disk space is wasted (same object modules are copied in more executables)
* virtual memory usage
* if a change is required, all executables must be relinked

Shared library: a single copy of object modules is shared by all programs requiring the modules
* first program loads the shared library, the other use the copy of the library that is already loaded in memory
* created with: gcc -fPIC ...-shared -o libshared.so

-fPIC = position-independent code: allows the code to be located at any virtual address at run time

soname = alias for a library name
* during static linking, the soname is embedded in the executable file instead of the real name; the purpose is to allow an executable to use a version of the shared library that is different (but compatible with) the library against which it was linked.
e.g:
libdemo.so.1 ---> libdemo.so.1.0.2

Usage in two steps
1. embedding the name of the shared library inside the executable during the link phase
2. dynamic linking: resolving the embedded lib name and loading the lib into memory

Plugins (loaded only when needed):
* dlopen(), dlsym(), dlclose()
* it's possible for a function x() in a shared library to access a function y() from main program (callback mechanism)
* possible to define functions automatically executed when a shared library is loaded/unloaded

Part 3. IPC and sockets

Chapter 43. IPC overview

IPC facilities:
* communication: pipes, FIFOs, sockets, shared memory
* synchronization: semaphores, file locks
* signal

Persistence of IPC objects:
* process: an IPC object exists only as long as it is held open by at least a process; pipe, FIFO, socket
* kernel: an IPC object exists until it's deleted or until shutdown
* file-system: an IPC object exists until it's deleted

Pipe:
* unidirectional byte stream; kernel-space
* pipe() –> fork() –> closing unused file descriptors:
- reader closes write descriptor; otherwise, when the other process closes its write descriptor, the reader will not see end-of-file and read() will block
- writer closes read descriptor; otherwise, writer will not receive SIGPIPE if the reader exits (kernel sends SIGPIPE if no process has an open read descriptor), the pipe will fill up and write() will block

Synchronize the action of parent and child processes:
* parent builds a pipe and creates children
* each child closes the write descriptor after it finishes its action
* parent's read() will return end-of-file

FIFO:
* similar to pipe, but it has a name within the file system and can be opened like a file (this allows the communication between unrelated processes)
* opening a FIFO for reading blocks until another process opens the FIFO for writing, and viceversa

Chapter 45. IPC

IPC objects message queues, semaphores and shared memory (first appeared on System V and have been ported to most UNIX implementations)
* each mechanism has a get(key) syscall: searches the set of all existing IPC objects for one with specified key; if a matching one is found, it will be returned, otherwise it will be created or error returned
* ctl() syscall performs a range of control operations for the object
* kernel persistence (exists until deletion/shut down)

Message queues:

1. System V:
* processes communicate via message queues, referred by message_queue_id
* it is not possible to read parts of the message, only full message (unlike pipes)
* messages can be retrieved from a queue in FIFO order or be retrieved by type
* messages need not to be read in the same order in which they were sent
Client-server with MQ:
1. single MQ between server – clients:
* client sends its pid to server
* server sends messages to that client using type=client_pid
* if a client doesn't read its messages, the queue will be clogged
2. per client MQ
* client creates a MQ and sends its id to server via server's MQ
2. POSIX:
* MQs are reference counted
* messages have an associated priority and are strictly queued and received in priority order
* a process can be asynchronously notified when a message is available

Semaphores:
* kernel-maintained integer whose value cannot drop below 0
* any attempt to decrease the value below 0 will block
* post(): increase value; wait(): decrease value
Posix:
* named (unrelated processes can access it) and unnamed (when shared between processes, must reside in a shared-memory region)

Shared memories:
* two or more processes share the same region of physical memory
* no kernel intervention is required, so it's faster than pipes
* the kernel chooses the address at which the segment is attached in the process' virtual space ---> the segment may reside at different virtual address in different processes ---> any references to addresses should be maintained as relative offsets, rather than as absolute pointers

Comparison of POSIX/System V IPC objects:
* System V objects are referred to by identifiers, rather than the file descriptors used by POSIX IPC
* POSIX IPC objects are reference-counted
* POSIX IPC interface is simpler (System V has additional programming complexity by using keys)
* System V is more portable

Chapter 49. Memory mappings

Memory mapping can be:
* file mapping (maps a region of a file directly into calling process' virtual memory) or anonymous mapping (pages of the mapping are initialized to 0)
* shared or private

therefore, there are 4 types:
1. private file mapping: contents of the mapping are initialized from a file region; usage: to initialize a region of memory from the contents of a file (initialize a process from a shared library)
2. private anonymous mapping: the purpose is to allocate large blocks of zero-filled memory; children inherit parent's mappings but COW is employed
3. shared file mapping: permits memory-mapped I/O (modifications are automatically written to this file, so it's a substitute for read()/write()) and allows unrelated processes to share a region of memory
4. shared anonymous mapping: when a child inherits the mapping after a fork(), the parent and the child share the same pages of RAM

Memory-mapped I/O:
* can provide better performance than I/O (carried with read()/write()) when performing repeated random access in a large file; for sequential access, traditional I/O performs better

To share memory between processes:
* a semaphore must be used to synchronize access to shared region
* create a shared-memory region: shm_open()
* set the size of the object via ftruncate()
* then map that region into your process's address space: mmap()

Chapter 50. Virtual Memory Operations

mlock(): lock part of process' virtual memory so that is guaranteed to be always in physical memory
* improve performance (no more page faults)
* security: because the page is never swapped out, no copy of the page ever exists

Avoid exposing sensitive information:
* erase the info from memory after being used (e.g reset password)
* use mlock() to prevent swap
* prevent core dumps using setrlimit()

mincore(): reports which pages in a virtual address range are currently residing in RAM

madvise(): informs the kernel about the process' likely usage of the pages: normal, random, sequential..

Chapter 55. File Locking

Using locks and stdio:
* perform file I/O (read() and write()) instead of stdio
* flush the stdio stream immediately after placing a lock on the file
* disable stdio buffering with setbuf()

Locking with flock():
* places a single lock (exclusive or shared) on an entire file or releases a lock
* locks are automatically released when the file descriptor is closed
* only advisory locks are placed

Locking with fcntl():
* places read/write locks on any region of the file (defined by length)
* placing a lock of different type (e.g W) in the middle of a region already locked (e.g R) will result in three locks: R W R

Other:
* mandatory locking: mount file-system with mand
* /proc/locks holds the list of all locks on the system

Running a single instance of a program
* the daemon creates a file in a directory and places a write lock on it
* open(lockfile) + unlink(lockfile)
* link(file, lockfile) + unlink(lockfile)

Chapter 56. Sockets

Networking layers:
Application (application data)
Transport (TCP segments)
Internet (IP datagram)
Link (data frames)

big/little endian = host byte order that store most/least significant byte first
network byte order = standard ordering used to transmit IP addresses and port numbers (big endian)

marshalling = the process of putting data into a standard format for transmission across network

High-load servers:

1. Pre-forked/pre-threaded servers:
* server precreates a fixed number of child processes (threads) = server pool
* each child in server pool serves a client and after that fetches the next client to be served and so on
Technique:
* parent creates the listening socket, fork() (so children inherit the file descriptor) and all children are doing accept() on the listening socket
* parent performs accept() and then passes the file descriptor (by sendmsg()/recvmsg()) to one of the children
* if the server pool consists of threads, the main thread does accept() and then informs a free server thread
2. Handling multiple clients from a single process:
* using I/O multiplexing, signal-driven I/O, epoll

3. Using server farms:
* usage of multiple server systems: round-robin load sharing (e.g DNS) or load-balancing (a single server routes incoming client requests to one of the member of the server farm)

The inetd Daemon:
* instead of running a separate daemon for each service (that would usually be doing nothing but waiting), a single process monitors a specified set of socket ports and starts other servers as required

Advanced Topics:
* shutdown(): provides more control over connection termination; we can forcibly shut down either or both halves of a bidirectional connection stream
* recv()/send() can be used to perform socket I/O and provide extra argument, flags
* sendfile() allows to efficiently copy the contents of a file to a socket (the file data is not copied into user space, like with read()/write())
* SO_REUSEADDR: set before bind() so that it will not fail because of TIME_WAIT state
* TCP_CORK: the application instructs the OS not to send any packets unless they are full, or the application signals the OS to send all pending data